## Slide 1: ARP Spoofing (Part I)

## Slide 2: Introduction
A computer connected to an IP/Ethernet has two addresses
  MAC address
    Hardware address / Physical address
    Globally unique address stored in the network card.
    Ethernet header contains the MAC addresses of the source and the destination computer.
  IP address
    Each computer in a network must have a unique IP address to communicate.
    Virtual and assigned by software.

## Slide 3
The Internet Layer (IP) communicates by constructing packets.
Packets are delivered by Ethernet.
  Adds an Ethernet header for delivery
  Splits the packets into frames
  Sends them down the cable to the switch.
  The switch then decides which port to send out the frame. By comparing the destination address of the frame to an internal table that maps port numbers to MAC addresses.

## Slide 4
When an Ethernet frame is constructed from an IP packet, which has no idea what the MAC address of the destination machine is.
The only information available is the destination IP address.
There must be a way to the Ethernet protocol to find the MAC address of the destination machine, given a destination IP.
This is where ARP, Address Resolution Protocol, comes in.

## Slide 5
Figure 8-1
Address resolution and Reverse address resolution
(obsolete)

## Slide 6
Figure 8-2
ARP
Notes: Demo for arp
"arp -d <ip_address>" to delete an entry

## Slide 7
Figure 8-3
Structure of an ARP packet:
Notes: Demo

## Slide 8
Figure 8-4
Encapsulation of ARP in an Ethernet Frame
Preamble (7 bytes) is used for synchronization
SFD (Start Frame Delimiter, 1 byte) indicates the start of the frame
(ARP)
Notes: Demo

## Slide 9
How ARP functions:
  Get IP address of target.
  Create a request ARP message
    Fill sender physical address
    Fill sender IP address
    Fill target IP address
    Target physical address is filled with 0
  The message is passed to the Ethernet layer where it is encapsulated in a frame.
    Source address: physical address of the sender.
    Destination address: broadcast address.

## Slide 10
  Every host or router on the LAN receives the frame.
    All machines check the ARP data.
    All machines except the one targeted drop the packet.
  The target machine replies with an ARP message that contains its physical address.
    A unicast message.
  The sender receives the reply message and knows the physical address of the target machine.

## Slide 11: A’s ARP request
ARP request packet
  Sender Hardware Address - A’s MAC address
  Sender Protocol Address – A’s IP address
  Target Hardware Address – Zeroes
  Target Protocol Address – B’s IP address
Ethernet layer
  Source Hardware Address – A’s MAC address
  Target Hardware Address – FF:FF:FF:FF:FF:FF

## Slide 12: B’s ARP reply
ARP reply packet
  Sender Hardware Address - B’s MAC address
  Sender Protocol Address – B’s IP address
  Target Hardware Address – A’s MAC address
  Target Protocol Address – A’s IP address
Ethernet layer
  Source Hardware Address – B’s MAC address
  Target Hardware Address – A’s MAC address

## Slide 13
  To avoid having to send an ARP request packet every time, a host can cache the IP and the corresponding host addresses in its ARP cache (or ARP table).
  Each entry in the ARP cache is usually “aged” so that the contents are erased if no activity occurs within a certain period.
  When a computer receives an ARP reply, it will update its ARP cache.
  ARP is a stateless protocol, most operating systems will update their cache if a reply is received, regardless of whether they have sent out an actual request.
Notes: Demo for arp
"arp -d <ip_address>" to delete an entry

## Slide 14: Target IP Address of ARP
Consider a network that each connected device is either a host or a router
When a device sends an ARP request to resolve the IP address to the MAC address of another device in the same network, there are 4 cases:
  Case 1: Host  Host
  Case 2: Host  Router
  Case 3: Router  Router
  Case 4: Router  Host
The following shows the target IP addresses of ARP request for the 4 cases

## Slide 15
Figure 8-5, Part I
Case 2. A host wants to send a packet to another host on another network. It must first be delivered to a router.
Notes: Demo for Case 2 – ping a computer outside the network, then check the target IP Address of the ARP Request

## Slide 16
Figure 8-5, Part II

## Slide 17: Proxy ARP
Proxy ARP is the process in which one system responds to the ARP request for another system.
In other words, A sends an ARP request to resolve the IP address of B. Instead of B, another host C responds to this ARP request.
  Imagine that A and B are in different networks and C is a router connecting these two networks
  When a router receives ARP requests from one network for hosts on another network, the router will respond with an ARP reply packet with the router’s MAC address.

## Slide 18: Proxy ARP
For example, suppose host A is in one network, host B is in another network, and router C connects these two networks.
  When host A sends an ARP request to resolve the IP address of host B, router C receives this packet.
  Router C sends an ARP reply to host A with its MAC address.
    In the ARP reply: B’s IP + C’s MAC address
  So host A will send all the packets destined for host B to router C.
  Router C will then forward these packets to host B.
  In this case, router C can use proxy ARP to route packets from host A to host B.

## Slide 19
Figure 8-6
ARP Request: What is the MAC address of 141.23.56.21?
ARP Reply from router: 141.23.56.21 is at <router's MAC address>

## Slide 20: References
Forouzan, “TCP/IP protocol Suite”., Chapter 8. (Background of ARP)