## Slide 1: ARP Spoofing (Part III)

## Slide 2: Man-in-the-Middle (MiM) Attack
A hacker inserts his computer between the communications path of two target computers.
The hacker will forward frames between the two target computers so communications are not interrupted.
E.g., Hunt, Ettercap etc.
  Can be obtained easily in many web archives.

## Slide 3
The attack is performed as follows:
  Suppose S is the hacker’s computer
  A and B are the targets
  S poisons the ARP caches of A and B.
    A associates B’s IP with S’s MAC.
    B associates A’s IP with S’s MAC.
  All of the traffic of A and B will then go to S first, instead of directly to each other.

## Slide 4
A
IP:10.0.0.1
MAC:aa:aa:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb:bb:bb
Hacker S
IP:10.0.0.3
MAC:cc:cc:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb:bb:bb
ARP cache
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa:aa:aa
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc:cc:cc

## Slide 5
A
IP:10.0.0.1
MAC:aa:aa:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb:bb:bb
Hacker S
IP:10.0.0.3
MAC:cc:cc:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc:cc:cc
ARP cache
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa:aa:aa
A’s cache is poisoned

## Slide 6
A
IP:10.0.0.1
MAC:aa:aa:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb:bb:bb
Hacker S
IP:10.0.0.3
MAC:cc:cc:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc:cc:cc
ARP cache
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa:aa:aa
Spoofed ARP reply
IP:10.0.0.1
MAC:cc:cc:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.1
MAC:cc:cc:cc:cc:cc:cc

## Slide 7
A
IP:10.0.0.1
MAC:aa:aa:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb:bb:bb
Hacker S
IP:10.0.0.3
MAC:cc:cc:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc:cc:cc
ARP cache
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc:cc:cc
B’s cache is poisoned

## Slide 8
A
IP:10.0.0.1
MAC:aa:aa:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb:bb:bb
Hacker S
IP:10.0.0.3
MAC:cc:cc:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc:cc:cc
ARP cache
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc:cc:cc
1. Message intended to send to B
2. Hacker
will relay the
message

## Slide 9
A
IP:10.0.0.1
MAC:aa:aa:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb:bb:bb
Hacker S
IP:10.0.0.3
MAC:cc:cc:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc:cc:cc
ARP cache
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc:cc:cc
2. Hacker will relay the message
1. Message
intended to
send to A

## Slide 10
  Aftermath:
    After the MiM attack, the target computers will continue to send frames to the hacker’s MAC address even after the hacker removes himself from the communication path.
    To perform a clean MiM attack, the hacker will restore the ARP entries of the target computers.
      In A’s ARP cache
        Associate B’s IP with B’s MAC address
      In B’s ARP cache
        Associate A’s IP with A’s MAC address

## Slide 11
Possible types of attacks
  Sniffing
    By using ARP spoofing, all the traffic from the target to the receiver can be directed to the hackers.
      It is now possible to perform sniffing even on a switched network.
    However, the hacker needs to forward the packet from the target to the original receiver
      So that the communication as seen by the target will not be interrupted

## Slide 12
  Broadcasting
    In the ARP cache of the target, if an entry is poisoned to the broadcast MAC address (FF:FF:FF:FF:FF:FF), all the traffic from the target to the corresponding receiver is broadcasted
      It is now possible to perform sniffing even on a switched network.
  Hijacking
    By using MiM attack, all the traffic of a TCP connection will go through the hacker.
    Now it is much easier to hijack the session as compared to the method we discussed earlier in TCP exploits.
Notes: Demo with ping

## Slide 13
  DoS
    Updating ARP caches with non-existing MAC addresses will cause frames to be dropped.
    Denial of Service attack (DoS)
      Suppose a hacker wants isolate a victim computer
      The hacker poisons the victim’s ARP cache entry in all other clients in the same network
      No one will be able to send packets to the victim due to incorrect MAC addresses
      This can be done easily by using Gratuitous ARP (see later for more details)
Notes: Demo with ping

## Slide 14
  Cloning
    A MAC address is only supposed to be unique.
      It is easy to change the MAC address on the OS level.
      It is also possible to change the MAC address of a network card (burn into the ROM).
    Suppose a hacker wants to act as the DNS server
      First, the hacker performs the DoS attack (on the previous page) on the DNS server by poisoning the DNS server’s ARP cache entry in all other clients with a fake MAC address
      Then, the hacker assigns himself this fake MAC address
      All other clients will wrongly think that the hacker is the DNS server

## Slide 15: Gratuitous ARP
Source and target IPs in the ARP request / reply are the same.
In form of broadcast.
Some implementations recognize it as a special case: a system sending updated information about itself to everybody, and hence update the ARP cache accordingly.
One packet can screw up the entire network.

## Slide 16: S’s spoofed Gratuitous ARP Reply
Assume S tries to impersonate B and compromise all computers in the LAN
Spoofed Gratuitous ARP reply packet
  Sender Hardware Address – S’s MAC address
  Sender Protocol Address – B’s IP address
  Target Hardware Address – FF:FF:FF:FF:FF:FF
  Target Protocol Address – B’s IP address
Ethernet layer
  Source Hardware Address – S’s MAC address
  Target Hardware Address – FF:FF:FF:FF:FF:FF
Notes: Demo

## Slide 17: S’s spoofed Gratuitous ARP Request
Assume S tries to impersonate B and compromise all computers in the LAN
Spoofed Gratuitous ARP request packet
  Sender Hardware Address – S’s MAC address
  Sender Protocol Address – B’s IP address
  Target Hardware Address – Zeroes
  Target Protocol Address – B’s IP address
Ethernet layer
  Source Hardware Address – S’s MAC address
  Target Hardware Address – FF:FF:FF:FF:FF:FF
Notes: Demo

## Slide 18: Remarks about ARP Spoofing
ARP spoofing attacks may not always be successful
Different systems may have different behavior
  In some systems, ARP spoofing can only succeed if there is already an existing entry in the ARP cache
  Some systems only accept ARP updates after a timeout period

## Slide 19: Defenses against ARP Spoofing
Use static ARP entries
  Cannot be updated.
  Spoofed ARP requests/replies are ignored.
  The ARP table needs a static hardcoded entry for each machine on the network.
  Large overhead
    Deploying these tables
    Keep the table up-to-date
  In the past, someone points out that Windows still accepts spoofed ARP replies and updates the static entry with the forged MAC.

## Slide 20
Arpwatch
  A free UNIX program that listens for ARP replies on a network.
  Build a table of IP/MAC associations and store it in a file.
  When a IP/MAC pair changes (flip-flop), an email is sent to an administrator.
  Some programs, such as Ettercap, cause only a few flip flops is difficult to be detected on a DHCP-enabled network, where flip flops occur at regular intervals.

## Slide 21
RARP Request
  Request the IP of a known MAC.
  In form of broadcast.
  MAC cloning can be detected, if multiple replies are received for a single RARP request.

## Slide 22: ARP Poisoning on the Switch
  A switch must keep a MAC table of all MAC addresses appear on each port.
  Some switches update the MAC table based on the source MAC address of the frames received from different ports.
    For example, if Port 3 receives a frame with source MAC address cc:cc:cc:cc:cc:cc, the MAC table will add the following entry:
      Port 3 – cc:cc:cc:cc:cc:cc

## Slide 23
It is possible to perform ARP spoofing attacks to poison the MAC tables in such switches.
  So that the hacker can receive all the frames that are intended to send to other computers in the same network.
  For example, the hacker at S (connecting Port 3) sends a frame with source MAC address of A (aa:aa:aa:aa:aa:aa), the MAC table may add the following entry:
    Port 3 – aa:aa:aa:aa:aa:aa
  So the switch will forward all the packets destined to A to the hacker at S via Port 3
Such an attack works on some switches only

## Slide 24
Countermeasures
  Port Security
    Also known as Port Binding or MAC Binding.
    A feature on some high-end switches.
    Prevents changes to the MAC tables of a switch.
      Unless manually performed by a network administrator.
    Not suitable for large networks and networks using DHCP.

## Slide 25: References
Sean Whalen, “An introduction to ARP Spoofing”, http://chocobospore.org/arpspoof.
Yuri Volobuev, “Playing redir games with ARP and ICMP”, it doesn’t seem to be published formally.
Forouzan, “TCP/IP protocol Suite”., Chapter 8. (Background of ARP)