## Slide 1: TCP Exploits (Part II)

## Slide 2: Connection Killing
A and B have a TCP connection running
A and S are on the same subnet
Host A
Host S
Host B

## Slide 3
Reset by RST
  TCP packets have flags that indicate the status of the packet.
  RST: used to reset a connection
  A RST packet is accepted only when the sequence number is correct.
  Idea of RST attack
    S waits for packets in a connection between A and B
    From a packet from A to B, S calculates the next sequence number that will be used by B from A’s ACK
    S (pretending to be B) fires a bogus RST packet to A with a correct sequence number.

## Slide 4
Actual attack (from the paper):
  Attacker S waits for a packet to get current SEQ/ACK. Several packets, as seen by S, are shown below. S is ready to send his RST after the packets.
From | To | SEQ | ACK | Flags | Window
A | B | 57E1F2A6 | B8BD7679 | AP | 3400
B | A | B8BD7679 | 57E1F2A8 | AP | 2238
A | B | 57E1F2A8 | B8BD767B | A | 3400
B | A | B8BD767B | 57E1F2A8 | AP | 2238
A | B | 57E1F2A8 | B8BD7691 | A | 3400

## Slide 5
  The attacker sends his bogus RST packets to A, with source IP address forged as B.
  In the particular attack, 2 RST packets were sent.
  The SEQ of the first packet is calculated from the first packet in the table on the previous page.
    But the first RST packet has been buffered somewhere on the system, because the Ethernet segment was busy.
  The SEQ of the second packet is calculated from the fifth packet in the table on the previous page.
    The second RST packet actually kills the connection.
From | To | SEQ | ACK | Flags | Window
B | A | B8BD7679 |  | R | 
B | A | B8BD7691 |  | R | 
[two bogus packets fired from S (pretending to be B)]

## Slide 6
Case Study
  Study the code in sniper-rst.c
  In the class the RST attack will be demonstrated.
  We will capture and study the packets for the attack by using Ethereal.
  Weakness of RST attack
    Cannot confirm that the attack is successful
Notes: Demo on telnet (both directions)
Demo on ssh

## Slide 7
Closing a connection by FIN
  FIN flag: indicate “no more data from sender”.
  Used when closing a connection down in a normal way.

## Slide 8
Four-way handshaking for terminating a connection normally
Image source: http://tcpip.marcolavoie.ca/Images/Figure_13.gif (partial)
Notes: Demo (exiting a telnet session)

## Slide 9
  Idea of FIN attack
    The attacker S constructs a spoofed FIN packet.
    The packet must contain the correct sequence number, so that it will be accepted by one of the two hosts.
      Similar to the RST attack, a sniffer is used to find out the expected sequence number.
    The host which accepted the packet would believe the (spoofed) sender did not have any data left.
    Following (real) packets would be ignored as they are considered bogus.
    The “beauty” of FIN attack is that after a FIN is sent, the other host always replies if it is accepted.
    The attacker can verify that the killing is successful.

## Slide 10
Actual attack (from the paper)
  Connection between A and B is running.
  The sniper is started on host S.
  S waits for a packet to take action
  Plus two bytes data.
From | To | SEQ | ACK | Flags | Window
A | B | 19C6B98B | 69C5473E | AP | 3400

## Slide 11
  Sniper detected it, and sends a bogus packet (S as B  A)
  Set SEQ as ACK of the above packet.
  S calculates his ACK as
    SEQ of the above packet + data length of that packet = 19C6B98B + 2 = 19C6B98D.
  This bogus packet is for S (pretending to be B) to tell A that the last packet is received, and no further data will be transmitted.
    If A trusts this bogus packet and has no remaining data to send, A will reply a packet with SEQ = 19C6B98D and ACK = 69C5473F
    But in our case study, A has remaining data to send (see next page)
From | To | SEQ | ACK | Flags | Window
B | A | 69C5473E | 19C6B98D | AF | 7C00
[bogus packet fired from S (pretending to be B)]
Notes: The packet from A to B (previous page):
SEQ = 19C6B98B
ACK = 69C5473E
Length = 2

## Slide 12
  Host A says: “Okay, you end the session, so here is my last data (A B).
  Host A now has flushed its buffer and on his turn to send the FIN packet (AB).
  S intercepts this packet and now knows the hosts fell for the spoof and the connection killing is successful.
From | To | SEQ | ACK | Flags | Window
A | B | 19C6B98D | 69C5473E | AP | 3400
A | B | 19C6B998 | 69C5473F | A | 3400
From | To | SEQ | ACK | Flags | Window
A | B | 19C6B998 | 69C5473F | AF | 3400
This packet contains the remaining data
This packet acknowledges the FIN packet
Notes: The packet from hacker (pretending to be B) to A (previous page):
SEQ = 69C5473E
ACK = 19C6B98D
Flag = FIN

## Slide 13
  S impersonated B, making A believe B had no further data. But B doesn’t know that and keep sending data
    Note that B is unware of S and still using SEQ = 69C5473E
From | To | SEQ | ACK | Flags | Window
B | A | 69C5473E | 19C6B98D | A | 3750
Notes: The packet from A to B (previous page):
SEQ = 19C6B998
ACK = 69C5473F
Flag = FIN

## Slide 14
  Host A has that connection closed, and thus thinks the real packets of B are bogus. So host A sends some RST packets.
  This goes on for a couple of packets.
From | To | SEQ | ACK | Flags | Window
A | B | 19C6B98D |  | R | 

## Slide 15
Case Study
  Study the code in sniper-fin.c
  In the class the FIN attack will be demonstrated.
  We will capture and study the packets for the attack by using Ethereal.
Notes: Demo on telnet (both directions)
Demo on ssh

## Slide 16: Detection and Prevention
Detection
  Notice and verify the change of MAC address of the packets
    Assume that the MAC address cannot be changed by the policy restriction
Prevention
  Use IPsec (E.g., IPsec VPN)
    Operating at the Internet layer
      Or Layer 3 in the OSI 7 layer model
    The transport mode (the default mode) encrypts the IP payload, which includes the TCP header that contains the sequence number and the acknowledgement number.

## Slide 17: Connection Hijacking
A and B have a TCP connection running (telnet)
A and S are on the same subnet
Host A
Host S
Host B

## Slide 18
  TCP separates good and faked packets by their SEQ/ACK numbers.
  B trusts the packets from A because of its correct SEQ/ACK numbers.
  If there was a way to mess up A’s SEQ/ACK, B would stop believing A’ real packets.
  S could then impersonate A, but using correct SEQ/ACK numbers from the perspective of B.
  S would now have taken over the connection, and sends “correct” data to B.

## Slide 19
  This is called hijacking the connection
    The same technique can be applied to hijack TELNET, FTP, RLOGIN etc.
  How could we mess up A’s SEQ/ACK numbers?
    Simply inserting a data packet into the stream at the right time (S as A B).
    B would accept this data, and update ACK number.
    A would continue to send it’s old SEQ numbers, as it’s unaware of our spoofed data.

## Slide 20
Actual Attack (from the paper)
  Attacker S examines with a sniffer
    The user is in an interactive shell via telnet
    The hacker starts hijack
  The following packet from A to B is detected
    A’s IP address: 166.66.66.1
    B’s IP address: 111.11.11.11
TCP Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-111.11.11.11.23
SEQ (hex): 5C8223EA ACK (hex): C34A67F6
FLAGS: -AP--- Window: 7C00
Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-111.11.11.11.23
45 E 00 . 00 . 29 ) CA . F3 . 40 @ 00 . 40 @ 06 . C5 . 0E . 9D . C1 . 45 E 3F ?
9D . C1 . 2A * 0B . 04 . 10 . 00 . 17 . 5C \ 82 . 23 # EA . C3 . 4A J 67 g F6 .
50 P 18 . 7C | 00 . 6D m 29 ) 00 . 00 . 6C l
~~~~
A  B

## Slide 21
  B echoes that data bytes (“l”)
  A acknowledges
TCP Packet ID (from_IP.port-to_IP.port): 111.11.11.11.23-166.66.66.1.1040
SEQ (hex): C34A67F6 ACK (hex): 5C8223EB
FLAGS: -AP--- Window: 2238
Packet ID (from_IP.port-to_IP.port): 111.11.11.11.23-166.66.66.1.1040
45 E 00 . 00 . 29 ) B5 . BD . 40 @ 00 . FC . 06 . 1E . 44 D 9D . C1 . 2A * 0B .
9D . C1 . 45 E 3F ? 00 . 17 . 04 . 10 . C3 . 4A J 67 g F6 . 5C \ 82 . 23 # EB .
50 P 18 . 22 " 38 8 C6 . F0 . 00 . 00 . 6C l
~~~~
TCP Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-111.11.11.11.23
SEQ (hex): 5C8223EB ACK (hex): C34A67F7
FLAGS: -A---- Window: 7C00
(data removed because irrelevant)
Previous packet from A to B:
SEQ (hex): 5C8223EA
ACK (hex): C34A67F6
LEN (hex): 1
A  B
B  A

## Slide 22
    Hacker’s program impersonates A with further data to B.
    Calculate SEQ/ACK based on the packet on page 5.
    Sends a few backspaces (0x08) and some enters (0x0A) to clean up the command line.
      May generate some error messages, but the program will handle it.
TCP Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-111.11.11.11.23
SEQ (hex): 5C8223EB ACK (hex): C34A67F6
FLAGS: -AP--- Window: 7C00
Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-111.11.11.11.23
45 E 00 . 00 . 32 2 31 1 01 . 00 . 00 . 45 E 06 . 99 . F8 . 9D . C1 . 45 E 3F ?
9D . C1 . 2A * 0B . 04 . 10 . 00 . 17 . 5C \ 82 . 23 # EB . C3 . 4A J 67 g F6 .
50 P 18 . 7C | 00 . AE . F5 . 00 . 00 . 08 . 08 . 08 . 08 . 08 . 08 . 08 . 08 .
0A . 0A .
[bogus packet from S (pretending to be A)]
Packet (page 20) from A to B:
SEQ (hex): 5C8223EA
ACK (hex): C34A67F6
LEN (hex): 1
S(A)  B

## Slide 23
  Here is the echo of the spoofed data from B
    ACK = 5C8223F5 = 5C8223EB + A
    The connection belongs to the hacker now
    The SEQ/ACK of A is completely messed up.
TCP Packet ID (from_IP.port-to_IP.port): 111.11.11.11.23-166.66.66.1.1040
SEQ (hex): C34A67F7 ACK (hex): 5C8223F5
FLAGS: -AP--- Window: 2238
Packet ID (from_IP.port-to_IP.port): 111.11.11.11.23-166.66.66.1.1040
45 E 00 . 00 . 3C < B5 . BE . 40 @ 00 . FC . 06 . 1E . 30 0 9D . C1 . 2A * 0B .
9D . C1 . 45 E 3F ? 00 . 17 . 04 . 10 . C3 . 4A J 67 g F7 . 5C \ 82 . 23 # F5 .
50 P 18 . 22 " 38 8 26 & 7C | 00 . 00 . 5E ^ 48 H 5E ^ 48 H 5E ^ 48 H 5E ^ 48 H
5E ^ 48 H 5E ^ 48 H 5E ^ 48 H 5E ^ 48 H 0D . 0A . 0D . 0A .
Previous bogus packet from S (pretending to be A) to B:
SEQ (hex): 5C8223EB
LEN (hex): A (i.e., 10 bytes)
Previous packet from B to A:
SEQ (hex): C34A67F6
LEN (hex): 1
B  A

## Slide 24
TCP Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-111.11.11.11.23
SEQ (hex): 5C8223EB ACK (hex): C34A67F7
FLAGS: -AP--- Window: 7C00
(data removed because irrelevant)
TCP Packet ID (from_IP.port-to_IP.port): 111.11.11.11.23-166.66.66.1.1040
SEQ (hex): C34A680B ACK (hex): 5C8223F5
FLAGS: -A---- Window: 2238
(data removed because irrelevant)
TCP Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-157.193.42.11.23
SEQ (hex): 5C8223EB ACK (hex): C34A67F7
FLAGS: -AP--- Window: 7C00
(data removed because irrelevant)
TCP Packet ID (from_IP.port-to_IP.port): 111.11.11.11.23-166.66.66.1.1040
SEQ (hex): C34A680B ACK (hex): 5C8223F5
FLAGS: -A---- Window: 2238
(data removed because irrelevant)
A  B
A  B
B  A
B  A
A keeps using old SEQ: 5C8223EB
B keeps asking for: 5C8223F5

## Slide 25
  At this point the real TELNET client’s session hangs, most people ignore this and re-login after a few secs.
  Hacker will now try to get on track of SEQ/ACK.
    Each time a packet “out of number” arrives at a host, the host should answer with correct SEQ/ACK.
    This provides the hacker with certainty that a lot of packets are going to be sent with correct (and not changing) SEQ/ACK numbers.
  After that, the hacker can send data that he wants to execute.

## Slide 26
  The hacker fires off the faked bash command
    Echo “echo HACKED” >> $HOME/.profile<ENTER>
TCP Packet ID (from_IP.port-to_IP.port): 166.66.66.1.1040-111.11.11.11.23
SEQ (hex): 5C8223F5 ACK (hex): C34A680B
FLAGS: -AP--- Window: 7C00
Packet ID (from_IP.port-to_IP.port): 166.66.66.1-111.11.11.11.23
45 E 00 . 00 . 4D M 31 1 01 . 00 . 00 . 45 E 06 . 99 . DD . 9D . C1 . 45 E 3F ?
9D . C1 . 2A * 0B . 04 . 10 . 00 . 17 . 5C \ 82 . 23 # F5 . C3 . 4A J 68 h 0B .
50 P 18 . 7C | 00 . 5A Z B6 . 00 . 00 . 65 e 63 c 68 h 6F o 20 22 " 65 e 63 c
68 h 6F o 20 48 H 41 A 43 C 4B K 45 E 44 D 22 " 20 3E > 3E > 24 $ 48 H 4F O
4D M 45 E 2F / 2E . 70 p 72 r 6F o 66 f 69 i 6C l 65 e 0A . 00 .
[bogus packet from S (pretending to be A)]
Previous packet from B to A:
SEQ (hex): C34A680B
ACK (hex): 5C8223F5
S(A)  B

## Slide 27
  Now wait for this data to be confirmed
    ACK = 5C8223F5 + 25 (37 bytes)
  The connection runs on.
  Now the hacker can execute more command
  Or finish the connection.
TCP Packet ID (from_IP.port-to_IP.port): 111.11.11.11.23-166.66.66.1.1040
SEQ (hex): C34A680B ACK (hex): 5C82241A
FLAGS: -AP--- Window: 2238
Packet ID (from_IP.port-to_IP.port): 157.193.42.11.23-157.193.69.63.1040
(data removed because irrelevant)
B  A
Previous bogus packet from hacker (pretending to be A) to B:
SEQ (hex): 5C8223F5
ACK (hex): C34A680B
LEN (hex): 25 (i.e., 37 bytes)

## Slide 28
Case Study
  Study the code in hijack.c
  In the class a telnet hijack will be demonstrated.
  We will capture and study the packets for the attack by using Ethereal.
Notes: Demo on telnet
Kill the telnet connection from the server side:
lsof –i tcp:23
kill <PID of the telnet connection>

## Slide 29: Detection and Tracing
Network traffic monitoring
  TCP session hijacking can be very noisy.
  Most attacks that can only inject and can’t stop one of the original communications from sending.
  Tools can be written to watch for anomalous traffic or behavior due to hijacking
    Such as connections being reset, “hanging”, or strange garbage appearing onscreen.
Notice and verify the change of MAC address of the packets

## Slide 30: Prevention
Encryption
  E.g. use SSH, SFTP, etc
  Even if a hacker hijacked your session, the hacker cannot execute any command easily.
Use IPsec
  Operating at the Internet layer
  The transport mode (the default mode) encrypts the IP payload, which includes the TCP header that contains the sequence number and the acknowledgement number.
Notes: Hijack demo on ssh

## Slide 31: Reference
Brecht Claerhout, “A short overview of IP spoofing: Part I”. This paper can be found in many web archives, but does not seem to be published formally.
The programs sniper-rst.c, sniper-fin.c, and hijack.c are extracted from this paper.